## Slide 1
FLUID | COMPONENT | DESIGN CODE | MATERIAL | INSULATED (Y/N) | OP. PARAMETER | CURRENT RISK RATING | Corrosion Group : Damage Mechanism Susceptible: Internal Shell General Corrosion External ATMOSPHERIC CORROSION
TYPE | SPEC | GR | T (֯C) | P (Mpa)
Air | Top Head | ASME VII DIV 1 | CS | SA-516 | 70L | N | 50 | 3.6 | LOW
Air | Shell | ASME VIII DIV 1 | CS | SA-516 | 70L | N | 50 | 3.6
Air | Bottom Head | ASME VIII DIV 1 | CS | SA-516 | 70L | N | 50 | 3.6
Air Receiver
V-001
INSPECTION METHOD | INSPECTION COVERAGE | DAMAGE MECHANISM
UTTM (Correction Factor) | 100% of TML Location – Refer TML as per Attachment | General Corrosion
VISUAL INSPECTION | External Visual Inspection (100% Coverage) With follow up by UT, RT, or pit gauge as required. | Atmospheric Corrosion
MLK PMT 10101

## Slide 2
FLUID | COMPONENT | DESIGN CODE | MATERIAL | INSULATED (Y/N) | OP. PARAMETER | CURRENT RISK RATING | Corrosion Group : Damage Mechanism Susceptible: Internal Cooling Water Corrosion External General Corrosion
TYPE | SPEC | GR | T (֯C) | P (Mpa)
CHILLED WATER | Top Head | ASME VII DIV 1 | Stainless Steel | SA-240 | 316L | no | 100.0 | 1.1 | LOW
CHILLED WATER | Shell | ASME VIII DIV 1 | Stainless Steel | SA-240 | 316L | no | 100.0 | 1.1
CHILLED WATER | Bottom Head | ASME VIII DIV 1 | Stainless Steel | SA-240 | 316L | no | 100.0 | 1.1
INSPECTION METHOD | INSPECTION COVERAGE | DAMAGE MECHANISM
UTTM | 100% of TML Location – Refer TML as per Attachment | Cooling Water Corrosion
VISUAL INSPECTION | External Visual Inspection (100% Coverage) With follow up by UT, RT, or pit gauge as required. | General Corrosion
V-002
Expansion Tank
MLK PMT 10102

## Slide 3
FLUID | COMPONENT | DESIGN CODE | MATERIAL | INSULATED (Y/N) | OP. PARAMETER | CURRENT RISK RATING | Corrosion Group : Damage Mechanism Susceptible: Internal Steam Condensate Corrosion External Corrosion Under Insulation(CUI)
TYPE | SPEC | GR | T (֯C) | P (Mpa)
Condensate | Top Head | ASME VII DIV 1 | Carbon Steel | SA-516 | 70 | no | 200.0 | 1000.0 | LOW
Condensate | Shell | ASME VIII DIV 1 | Carbon Steel | SA-516 | 70 | no | 200.0 | 1000.0
Condensate | Bottom Head | ASME VIII DIV 1 | Carbon Steel | SA-516 | 70 | no | 200.0 | 1000.0
INSPECTION METHOD | INSPECTION COVERAGE | DAMAGE MECHANISM
EMAT | 100% of TML Location – Refer TML as per Attachment 1 | General Corrosion
VISUAL INSPECTION | External Visual Inspection (100% Coverage) And Remove >5% of suspected area (as per Attachment 2). And Follow up by UT, RT or pit gauges as required if visual inspection reveal CUI as necessary | CUI
V-003
Condensate Vessel
MLK PMT 10103

## Slide 4
FLUID | COMPONENT | DESIGN CODE | MATERIAL | INSULATED (Y/N) | OP. PARAMETER | CURRENT RISK RATING | Corrosion Group : Damage Mechanism Susceptible: Internal Shell General Corrosion External CUI-CLSCC
TYPE | SPEC | GR | T (֯C) | P (Mpa)
HOT WATER | Head | ASME VII DIV 1 | Stainless Steel | A-240 | 304L | yes | 120.0 | 4.0 | LOW
HOT WATER | Shell | ASME VIII DIV 1 | Stainless Steel | A-240 | 304L | yes | 120.0 | 4.0
INSPECTION METHOD | INSPECTION COVERAGE | DAMAGE MECHANISM
UTTM (Correction Factor) | 100% of TML Location – Refer TML as per Attachment 1 | General Corrosion
VISUAL INSPECTION | 100% external visual inspection prior to insulation removal Ref: 1. General VI. Ext Inspection Checklist 2. CUI-CLSCC inspection checklist. And For suspected area where accessible: > 5% DPT or Eddy Current Testing with UT follow up of all relevant indication. | CUI-CLSCC
DPI (High Temp) | For suspected area where accessible: > 5% DPT or Eddy Current Testing with UT follow up of all relevant indication as per Attachment 2 | CUI-CLSCC
V-004
Hot Water System
MLK PMT 10104

## Slide 5
FLUID | COMPONENT | DESIGN CODE | MATERIAL | INSULATED (Y/N) | OP. PARAMETER | CURRENT RISK RATING | Corrosion Group : Damage Mechanism Susceptible: Internal Shell Side Cooling Water Corrosion Internal Tube Side Sulfuric Acid Corrosion External Shell Side General Corrosion External Tube Side CUI-CLSCC
TYPE | SPEC | GR | T (֯C) | P (Mpa)
WATER | Top Channel (Tube Side) | ASME VII DIV 1 | Stainless Steel | SA-240 | 316 | yes | 150.0 | 4.0 | LOW
AIR GAS/SULPHUR OXIDE | Shell | ASME VIII DIV 1 | Stainless Steel | SA-240 | 316 | yes | 150.0 | 4.0
WATER | Bottom Channel (Tube Side) | ASME VIII DIV 1 | Stainless Steel | SA-240 | 316 | yes | 150.0 | 4.0
INSPECTION METHOD | INSPECTION COVERAGE | DAMAGE MECHANISM
UTTM | 100% of TML Location – Refer TML as per Attachment 1 | General Corrosion Sulfuric Acid Corrosion
VISUAL INSPECTION | 100% external visual inspection prior to insulation removal Ref: 1. General VI. Ext Inspection Checklist 2. CUI-CLSCC inspection checklist. And For suspected area where accessible: > 5% DPT or Eddy Current Testing with UT follow up of all relevant indication. | General Corrosion CUI-CLSCC
DPI (High Temp) | For suspected area where accessible: > 5% DPT or Eddy Current Testing with UT follow up of all relevant indication as per Attachment 2 | CUI-CLSCC
V-005
Absorber for Neutralization of Acid Gases
MLK PMT 10105

## Slide 6
FLUID | COMPONENT | DESIGN CODE | MATERIAL | INSULATED (Y/N) | OP. PARAMETER | CURRENT RISK RATING | Corrosion Group : Damage Mechanism Susceptible: Internal Steam Condensate Corrosion External Corrosion Under Insulation(CUI)
TYPE | SPEC | GR | T (֯C) | P (Mpa)
WATER & STEAM | Head | ASME VII DIV 1 | Carbon Steel | SA-283 | C | no | 150.0 | 350.0 | LOW
WATER & STEAM | Shell | ASME VIII DIV 1 | Carbon Steel | SA-283 | C | no | 150.0 | 350.0
INSPECTION METHOD | INSPECTION COVERAGE | DAMAGE MECHANISM
UTTM (Correction Factor) | 100% of TML Location – Refer TML as per Attachment 1 | General Corrosion
VISUAL INSPECTION | External Visual Inspection (100% Coverage) And Remove >5% of suspected area (as per Attachment 2). And Follow up by UT, RT or pit gauges as required if visual inspection reveal CUI as necessary | CUI
V-006
Thermal Deaerator
MLK PMT 10106

## Slide 7
FLUID | COMPONENT | DESIGN CODE | MATERIAL | INSULATED (Y/N) | OP. PARAMETER | CURRENT RISK RATING | Corrosion Group : Damage Mechanism Susceptible: Internal Shell Side General Corrosion Internal Tube Side General Corrosion External General Corrosion
TYPE | SPEC | GR | T (֯C) | P (Mpa)
Vent Gas | Channel (Tube Side) | ASME VII DIV 1 | Stainless Steel | SA-240 | 316.0 | yes | 535.0 | 0.5 | LOW
Vent Gas | Shell | ASME VIII DIV 1 | Stainless Steel | SA-240 | 316.0 | yes | 335.0 | 0.5
INSPECTION METHOD | INSPECTION COVERAGE | DAMAGE MECHANISM
EMAT | 100% of TML Location – Refer TML as per Attachment 1 | General Corrosion
VISUAL INSPECTION | 100% external visual inspection Ref: 1. General VI. Ext Inspection Checklist | General Corrosion
H-001
Cooling of Steam- Gas Mix at The Exit of the Reactor
MLK PMT 10107

## Slide 8
FLUID | COMPONENT | DESIGN CODE | MATERIAL | INSULATED (Y/N) | OP. PARAMETER | CURRENT RISK RATING | Corrosion Group : Damage Mechanism Susceptible: Internal Shell Side Sulfuric Acid Corrosion Internal Tube Side Cooling Water Corrosion External General Corrosion
TYPE | SPEC | GR | T (֯C) | P (Mpa)
ALKALINE WATER | Channel | ASME VII DIV 1 | Stainless Steel | SA-403 | WP316 | no | 100.0 | 10.0 | LOW
CHILLED WATER | Shell | ASME VIII DIV 1 | Stainless Steel | SA-312 | TP316 | no | 150.0 | 10.0
INSPECTION METHOD | INSPECTION COVERAGE | DAMAGE MECHANISM
UTTM | 100% of TML Location – Refer TML as per Attachment 1 | Sulfuric Acid Corrosion Cooling Water Corrosion
VISUAL INSPECTION | 100% external visual inspection Ref: 1. General VI. Ext Inspection Checklist | General Corrosion
H-002
Gas Scrubber Cooler
MLK PMT 10108

## Slide 9
FLUID | COMPONENT | DESIGN CODE | MATERIAL | INSULATED (Y/N) | OP. PARAMETER | CURRENT RISK RATING | Corrosion Group : Damage Mechanism Susceptible: Internal Shell Side General Corrosion Internal Tube Side Cooling Water Corrosion External General Corrosion
TYPE | SPEC | GR | T (֯C) | P (Mpa)
Chilled Water | Channel | ASME VII DIV 1 | Stainless Steel | SA-403 | 316 | yes | 90.0 | 8.0 | LOW
REFLUX WATER | Shell | ASME VIII DIV 1 | Stainless Steel | SA-312 | TP316 | yes | 90.0 | 8.0
INSPECTION METHOD | INSPECTION COVERAGE | DAMAGE MECHANISM
UTTM | 100% of TML Location – Refer TML as per Attachment 1 | General Corrosion Cooling Water Corrosion
VISUAL INSPECTION | 100% external visual inspection Ref: 1. General VI. Ext Inspection Checklist | General Corrosion
H-003
Cooling of Water on Irrigation of An Absorber
MLK PMT 10109

## Slide 10
FLUID | COMPONENT | DESIGN CODE | MATERIAL | INSULATED (Y/N) | OP. PARAMETER | CURRENT RISK RATING | Corrosion Group : Damage Mechanism Susceptible: Internal Shell (Tube Side) General Corrosion Internal Channel Head (Tube Side) Cooling Water Corrosion External General Corrosion
TYPE | SPEC | GR | T (֯C) | P (Mpa)
CHILLED WATER | Channel (Tube Side) | ASME VII DIV 1 | Stainless Steel | SA-240 | 316 | yes | 200.0 | 10.0 | LOW
REFLUX WATER | Shell | ASME VIII DIV 1 | Stainless Steel | SA-240 | 316 | yes | 210.0 | 12.0
INSPECTION METHOD | INSPECTION COVERAGE | DAMAGE MECHANISM
UTTM | 100% of TML Location – Refer TML as per Attachment 1 | General Corrosion Cooling Water Corrosion
VISUAL INSPECTION | 100% external visual inspection Ref: 1. General VI. Ext Inspection Checklist | General Corrosion
H-004
Reflux Condensor of Drying Tower
MLK PMT 10110